## Slide 1
Solar Performance Analyzer
Himshikhar Data Science Track
By-Khushboo Khilnaney (742)
Satwik Srijan (722)
Ujjawal Verma (723)

## Slide 2
Problem & Real-World Impact
Invisible Output Gaps
Solar plants suffer from silent underperformance due to fouling, thermal derating, and localized inverter faults that go entirely unnoticed in aggregate data.
Undetected faults lead to compounding energy losses, severely reducing asset ROI and grid reliability.
Our solution is an automated, machine-learning-driven analyzer that translates raw weather and generation data into actionable alerts and highly accurate expected generation curves.

## Slide 3
Data Sources
Telemetry data heavily integrating AC power output alongside strictly monitored weather inputs: solar irradiation, module temperature, and ambient temperature.
Granularity
Time-series data is continuously captured and streamed at strict 15-minute intervals, providing high-resolution visibility into transient anomalies.
Data Cleaning
Strategic removal of nighttime noise (irradiation < 0.02) and advanced imputation for missing values to ensure the model focuses purely on daylight generation constraints.
Dataset & Ingestion

## Slide 4
1. Ingestion & Pipeline
Real-time data pipeline streaming from plant sensors directly into the localized data warehouse.
2. Data Processing
Applying automated capacity normalization and feature engineering (including rolling averages and time-of-day offsets).
3. ML Inference & Diagnostics
Models predict expected output while the diagnostic engine performs gap analysis, peer benchmarking, and persistence filtering.
4. Actionable UI
Business-friendly dashboard detailing exact energy loss and direct financial impact.
Workflow & Architecture

## Slide 5
Standardizing Output
To evaluate large and small inverters on identical scales, we utilize the industry-standard "Performance Ratio."
This transforms an absolute kW prediction into a dimensionless efficiency problem (ranging from 0 to ~1), neutralizing scale biases.
Capacity is estimated aggressively as the 95th percentile of AC power during optimal high-irradiance readings.
Mathematical Formulation
Inverter Capacity Estimation:
Performance Ratio Transformation:
Target Normalization

## Slide 6
The Ensemble Model
The core predictor is a Random Forest Regressor—an ensemble of decision trees used to minimize variance and aggressively prevent overfitting.
By using bootstrap-resampled data and random feature subsets at every node split, the forest maintains robustness against noise.
Each individual tree recursively splits the feature space to minimize the Mean Squared Error (MSE) within resulting leaves.
Variance Minimization
Ensemble Average:
Split Gain Strategy:
Random Forest Regression

## Slide 7
Contamination Bias Fix
Standard regression minimizes errors over all data. Including faulty periods pulls the fitted curve downward, causing leverage bias.
We deploy a two-pass "healthy data" trim—a crude but highly effective robust regression technique similar to RANSAC.
Refitting solely on this subset forces the model to estimate what *should* happen during healthy states, rather than average operation including breakdowns.
Trimming Logic
Residual Calculation (Pass 1):
Healthy Set Refit:
Robust Regression Trim

## Slide 8
Hard-Threshold Classification
We apply deliberate, non-learned threshold logic to evaluate deviations from expected output.
This design decision ensures the diagnostic engine remains highly auditable and deterministic, generating statuses operations teams can blindly trust.
By classifying percentage gaps into actionable buckets (Critical vs. Warning), operators instantly triage severity.
Deterministic Status Logic
Percentage Deviation:
Threshold Triage:
Underperformance: Gap %

## Slide 9
Nonparametric Anomaly Detection
At any given timestamp, all inverters within a specific solar plant theoretically share identical localized weather conditions.
We benchmark using the median rather than the mean. This is crucial because if 2 out of 22 inverters are offline, a simple mean would drastically lower expected levels.
This robust central tendency prevents failing hardware from masking adjacent failures.
Deviation Calculation
Peer performance comparison:
If the deviation metric breaches a 20% limit against healthy peers, it reinforces individual inverter fault alarms.
Peer Benchmarking

## Slide 10
Run-Length Encoding
This is discrete-time signal processing, functioning as a debouncing filter to suppress transient noise like isolated passing clouds.
Alerts physically trigger only when the negative run length extends to 4+ consecutive intervals (1 full hour).
State changes are tracked cleanly:
Persistence Detection

## Slide 11
Demonstration

## Slide 12
Demonstration

## Slide 13
Demonstration

## Slide 14
Demonstration

## Slide 15
15
Min Integration Intervals
Translating Ratios to Revenue
We transform abstract performance ratios directly into actionable financial metrics using a discretized left-Riemann-sum over 15-minute intervals.
By linearly scaling this lost kW volume against user-defined energy tariffs, asset managers can instantly prioritize maintenance by true monetary value.
Business & Financial Impact

## Slide 16
Global Importance
Random Forest variance reduction reliably identifies irradiation as the ~99% dominant predictive feature—providing a critical physics-based sanity check.
Local Explainability (TreeSHAP)
Shapley values decompose individual predictions into exact per-feature contributions, enabling precise root-cause diagnostics per alert.
Explainable AI (XAI)

## Slide 17
Model Performance Metrics
Metric | Definition | Importance for Operations
MAE | Mean Absolute Error – average absolute difference between predicted and actual values. | Provides an easily interpretable measure of average prediction error in kW, helping operators understand typical forecasting deviation.
MSE | Mean Squared Error – average of the squared differences between predicted and actual values. | Penalizes larger prediction errors more heavily, making it useful for identifying models that occasionally produce significant deviations.
RMSE | Root Mean Square Error – square root of the Mean Squared Error. | Measures the typical prediction error in the original unit (kW), making it practical for evaluating real-world model accuracy and operational reliability.
R² | Coefficient of Determination – proportion of variance in the target explained by the model. | Indicates how well the model captures changes in solar power output. Higher R² values reflect stronger predictive performance and greater confidence in operational decisions.

## Slide 18
Metric | Value | 
MAE | 27.6 | 
MSE | 9010.89 | 
RMSE | 0.9143 | 
R^2 | 0.9143 | 
Result Metrics

## Slide 19
Hardcoded Thresholds: The persistence interval, gap thresholds (15%/30%), peer deviation limit (20%), and overheat cutoffs (55°C) are intentional judgment calls prioritizing auditable business logic over complex statistical fits.
Data Dependency: Regression predictions rely entirely on localized telemetry. Pyranometer sensor drift or misalignment can artificially mimic widespread inverter hardware failure.
Responsible Use (Human-in-the-Loop): This diagnostic engine is a high-level decision-support system. It dictates financial prioritization but physical interventions still strictly require manual validation.
Limitations & Responsible Use

## Slide 20
Powering the Future
By fusing robust machine learning regression, localized explainability, and deterministic signal processing, we successfully translate raw solar noise into actionable financial intelligence.
Future Goal: Dynamic 1-minute streaming telemetry & live grid-pricing APIs.

## Slide 21
https://assets.solarplaza.com/filer_public_thumbnails/filer_public/89/9a/899a6abc-dd7a-42af-a00d-f6c0525580fc/cms_page_media2016114dirty.jpg__800x223_q85_subsampling-2.jpg
Source: www.solarplaza.com
https://cdn.dribbble.com/userupload/47366409/file/c8aa4cbe0605eee5edbf9d1880b06894.png?format=webp&resize=400x300&vertical=center
Source: dribbble.com
https://static.vecteezy.com/system/resources/thumbnails/078/527/329/small/neon-sound-waves-and-glowing-audio-wave-graph-vector.jpg
Source: www.vecteezy.com
Image Sources

## Slide 22
Contribution
Ujjawal Verma - ML (55%)
Khushboo Khilnaney- Report, PPT,Demo,ML(20%)
Satvik Srijan – ML(25%)

## Slide 23
THANK YOU!